## Slide 1: Network Automation in NORDUnet with NSO
SIG-NOC, CERN, April 2017
Henrik Thostrup Jensen < htj at nordu net >

## Slide 2: Background
Why do automation?
We were doing a lot of similar configuration manually or semi-manually
  Network was growing, especially peering
  Repetitive work sucks
  Manual errors becomes an issue
We selected the NCS tool from Tail-F
In this talk:
  NCS / NSO overview
  Automation in NORDUnet (and SUNET)

## Slide 3: NCS / NSO
NCS = Network Configuration System
Commercial product, created by Tail-F
Tail-F was acquired by Cisco in 2014
  NCS was renamed to NSO
  NSO = Network Service Orchestrator

## Slide 4: NSO Overview
Router
Router
Router
netconf
netconf
netconf
NSO
Transactions over multiple devices
Juniper-style CLI with all devices in one tree
Device configuration / capability described with yang schema
Netconf proxy enables communication with CLI/TL1 devices
cli
http/json

## Slide 5: NSO Services
Unified CLI is not enough
NSO supports services as an abstraction
  Schema + code to create configuration
  Service schema = high level service description
  Code transforms service into router configuration
    Code has to be written - no magic
htj@ncs> show configuration services vpn uts-fre-funet
side-a {
router se-fre;
interface et-2/1/0;
}
side-b {
router no-uts;
interface xe-1/0/1;
}
vlan 11;

## Slide 6: Fastmap
Writing service code for creation, update, and deletion is difficult to get right
With fastmap one only has to write code for service creation
  create(service) -> configuration
NSO will save the result of the create
On update, NSO will re-run create and do a diff with the previous result
  Only changes are send to the routers
Works very well for static configuration
  Doesn’t work that well for dynamic output (filters)

## Slide 7: NSO in NORDUnet
NORDUnet & NSO
  Templates
  Services
    Peering
    Customers
    User management
    VPN setup

## Slide 8: Templates
A simple way for engineers to re-use configuration across devices
  Good for simple stuff (no software development)
htj@ncs> show configuration devices template iBGP
config {
junos:configuration {
protocols {
bgp {
precision-timers;
log-updown;
group SUNET-CORE {
neighbor "{$ipv4_neighbor}" {
description "{$neighbor}";
}
}
group SUNET-CORE-v6 {
neighbor "{$ipv6_neighbor}" {
description "{$neighbor}";
}
}
}
}
}
}
htj@ncs% request devices device umu-r1 apply-template template-name iBGP

## Slide 9: Peer Service
NORDUnet has fairly big peering infrastructure
  About 650 networks, 3000 bgp sessions
as-path filters and prefix limits for all peers
  Because routing security
  Should be updated several times a week
  1.3M lines of configuration on ~25 routers
  85% of that is as-path filters 
Maintaining this manually is… tricky

## Slide 10: Peer Service
Actual service example
  No router, just IX (IX -> router mapping done elsewhere)
  No vendor specific stuff
htj@ncs> show configuration services service AS11798
type {
bgp-peer {
as 11798;
description "Ace Data Centers, Inc.";
as-macro4 AS-ACEDATACENTERS;
as-macro6 AS-ACEDATACENTERS;
prefix-limit 120;
prefix6-limit 10;
exchange-points EQX-CHI {
peering 206.223.119.174;
peering 2001:504:0:4:0:1:1798:1;
}
}
}

## Slide 11: Peer Service
What happens when a peer service is setup?
  BGP neighbor configuration
  Policy for bgp neighbor
  AS path filter is created
    Populated via bgpq3 (can manually add as numbers)
  Even a simple service will often produce +100 lines of configuration
Transparency and abstraction when possible
  Peering service supports both Juniper and Arista
  IP v4/v6 differences are handled automatically
    If things can be shared they will, otherwise not

## Slide 12: Peer Service
Setting up a peer
  Setup peering across several routers in less than a minute!
ncs> configure
ncs% edit services service AS10474 type bgp-peer
ncs% set as 10474
ncs% set exchange-points LINX
ncs% request retrieve-info
root@ncs% show
as 10474;
description "Optinet, South Africa";
as-macro4 AS-OPTINET;
as-macro6 AS-OPTINET;
prefix-limit 1265;
prefix6-limit 63;
exchange-points LINX {
peering 195.66.224.149;
peering 2001:7f8:4::28ea:1;
}
ncs% commit

## Slide 13: Customer Service
Fairly similar to peering service
More flexible in what should be created or not
  Customers often have specific policies / communities
  Options to create prefix filter, policy, bcp38 filter, etc.
service AS2847 {
type {
bgp-customer {
as 2847;
import-rules [ mark-external reject-martians litnet-in ];
export-rules [ export-aggregates reject-badroute transit-out ];
description LITNET;
as-macro4 AS-LITNET;
as-macro6 AS-LITNET;
prefix-limit 200;
routers de-hmb {
peering 109.105.98.127;
peering 2001:948:2:1a::2;
}
}
}
}

## Slide 14: VPN Service
L2 tunnel from one port to another port
Supports trunk, vlan, vlan-rewrite
  Automatically creates units on interfaces
MPLS across routers, interface-switch for router-local VPNs
Integrated with our network inventory
  Service is registered and documented automatically on commit
htj@ncs> show configuration services vpn uts-fre-funet
side-a {
router se-fre;
interface et-2/1/0;
}
side-b {
router no-uts;
interface xe-1/0/1;
}
vlan 11;
service-id NU-S800029;
vrf-target target:2603:4242001028;
route-distinguisher 2603:1028;
Automatically assigned

## Slide 15: SunetC Network
SunetC is the new Swedish R&E network
  Somewhat special (in a good, but annoying way)
  DWDM cards in routers
  Unified provider and customer border routers
Provider router
Provider router
Spine switch
Spine switch
Spine switch
Customer router
Customer router
Traditional
Spine switch
Spine switch
Spine switch
Shared router
Shared router
SunetC
Less equipment 
Lower cost 
Shared equipment 

## Slide 16: SSH User Service
htj@ncs> show configuration services ssh-users
staff {
ldap-group ndn-netadmin {
user-class super-user;
device-group SUNET-ALL;
}
}
system-users ni {
description NI;
ssh-keys [ "ssh-rsa … ];
user-class SUNETCVIEW;
}
customer-users BTH-bmt {
description "Bjorn Mattsson";
ssh-keys [ "ssh-rsa … ];
write-device-group [ BTH ];
read-device-group [ SUNET-CORE ];
expire-date 2017-10-01;
}
support-users jtac {
description JTAC;
ssh-keys [ "ssh-rsa … ];
expire-date 2017-12-01;
read-device-group [ SUNET-CORE SUNET-CPE-ALL ];
user-class super-user;
devices [ fln4-r1 kir3-r2 lba-r1 sva-r1 ];
}

## Slide 17: Experiences
NSO is not a perfect system
  Tends to see routers as configuration databases
  Transactional system has severe limitations
  Not a great tool for troubleshooting
JunOS is not perfect either
  Netconf stack is the main issue, rpd issues as well
Network automation allows you to shoot yourself in the feet and hands simultaneously
  Having people configure everything manually isn’t exactly unproblematic either
Some things are not possible without automation
Some things are not worth the time / investment

## Slide 18: Summary
NORDUnet & SUNET has a fair amount of automation in their networks
  But not everything is automated
Further reading
  Our schema and code is open source
    https://git.nordu.net/?p=ndn-ncs.git;a=summary
  Information about the new SUNET network
    Including router baseline configuration
    https://www.sunet.se/blogg/a-trip-down-the-non-volatile-memory-lane/