## Slide 1
Marko Eremija
5th SIG NOC meeting, Geneva
RADIUS infrastructure monitoring
26 - 27 April 2017
User Services Engineer

## Slide 2: eduroam in Serbia
eduroam project in Serbia started at the end of 2009
Process of connecting AMRES institutions to eduroam service and installation of equipment started in 2010
AMRES applied for donation from NATO SPS NIG programme (Networking Infrastructure Grant) with project “AMRES Access Infrastructure Establishment” and got the donation in 2010
new project is currently under way

## Slide 3: What is being monitored?
eduroam monitoring system is incorporated into our in-house network monitoring system – NetIIS
AMRES institutions network administrators are already using NetIIS in their every day technical activities
Monitoring and reporting
  RADIUS servers (institutional RADIUS servers and Federation Top Level RADIUS – FTLR servers)

## Slide 4: NetIIS – Networking Information and Monitoring System
directory
location
users and group of users
groups
device
monitor
alarm
action
NetIIS is a web based networking information and monitoring system
All objects from external world are presented in a way that is easy to understand
The objects are hierarchically organized and presented by a tree

## Slide 5: NetIIS – Networking Information and Monitoring System
Every institution has its own location in NetIIS infrastructure, under which eduroam directory is placed
eduroam data and infrastructure elements that are being monitored are stored in that directory

## Slide 6: Monitoring and reporting - RADIUS servers
Testing availability of a RADIUS server over the network
  Ping RADIUS server IP address
Testing operability of RADIUS servers :
  eapol_test program from the WPA supplicant software is used http://w1.fi/wpa_supplicant/
  Shell script on the NetIIS runs the eapol_test
  EAP-TTLS and PEAP tunnels can be tested
In case of a test failure, the alarm is triggered and mail notifications are sent to the technical contacts of the corresponding institution
Notes: Možda dodati i priču za eapol_test skriptu, tj. screenshot sa Netisa

## Slide 7: Monitoring and reporting - RADIUS Ping

## Slide 8
NetIIS
FTLR
IdP RADIUS
RP RADIUS
EAP TTLS IdP + FTLR
EAP TTLS RP
EAP TTLS IdP
EAP TTLS Proxy
Monitoring and reporting - RADIUS operability testing

## Slide 9: Monitoring and reporting - RADIUS IdP
EAP TTLS
test@inst.ac.rs
NetIIS
inst.ac.rs
IdP RADIUS
Operability of EAP tunnel established directly with the IdP RADIUS server is tested
eapol_test

## Slide 10: Monitoring and reporting - RADIUS IdP
RADIUS Status and Delay charts (period of 15 days)

## Slide 11: Monitoring and reporting - RADIUS IdP + FTLR
Operability of EAP tunnel established over the FTLR server to the IdP RADIUS server is tested
eap-ttls
test@inst.ac.rs
eapol_test
eapol_test
NetIIS
FTLR
inst.ac.rs
IdP RADIUS

## Slide 12: Monitoring and reporting - RADIUS IdP + FTLR
Radius Status and Delay charts (period of 15 days)

## Slide 13: Monitoring and reporting - RADIUS RP
Operability of EAP tunnel established over the institutional RADIUS sever and FTLR server to the monitor RADIUS server is tested
RP RADIUS
monitor
RADIUS
FTLR
eap-ttls
test@monitor.eduroam.ac.rs
eapol_test
NetIIS
monitor.eduroam.ac.rs
RADIUS

## Slide 14: Monitoring and reporting - RADIUS RP
RADIUS Status and Delay charts (period of 24 hours)

## Slide 15: Monitoring and reporting - FTLR
The availability and operability of FTLR server are tested
monitor
RADIUS
FTLR
eapol_test
NetIIS
monitor.eduroam.ac.rs
IdP RADIUS
eap-ttls
test@monitor.eduroam.ac.rs

## Slide 16: Groups of monitors – Institutional RADIUS servers

## Slide 17: Groups of monitors – FTLR

## Slide 18
marko.eremija@amres.ac.rs
Any Questions ?