## Slide 1
Click to edit Master title style
Click to edit Master text styles
  Second level
    Third level
      Fourth level
        Fifth level
18/06/2020
1
GEANT Operational Challenges
Coping without WAN-PHY
& Using BFD
www.geant.org
Tony Barber
Head of GÉANT Operations Centre & CERT

## Slide 2: WAN PHY Standard – 10GBase-W
At the time that the 10 Gigabit Ethernet standard was developed, interest in 10GbE as a wide area network (WAN) transport led to the introduction of a WAN PHY for 10GbE. The WAN PHY encapsulates Ethernet packets in SONET OC-192c frames and operates at a slightly slower data-rate (9.95328 Gbit/s) than the local area network (LAN) PHY.
The WAN PHY uses the same 10GBASE-S, 10GBASE-L and 10GBASE-E optical PMDs as the LAN PHYs and is designated as 10GBASE-SW, 10GBASE-LW or 10GBASE-EW. Its 64b/66b PCS is defined in IEEE 802.3 Clause 49 and its PMD sublayers in Clauses 52. It also uses a WAN Interface Sublayer (WIS) defined in Clause 50 which adds extra encapsulation to format the frame data to be compatible with SONET STS-192c.[22]
The WAN PHY was designed to interoperate with OC-192/STM-64 SDH/SONET equipment using a light-weight SDH/SONET frame running at 9.953 Gbit/s.

## Slide 3: WAN-PHY in GÉANT
WANPHY used extensively on PARTNER 10G links
WANPHY used on all backbone links until recently
Why WANPHY ?
  Troubleshooting/ALS

## Slide 4: Engineers Like WAN PHY for troubleshooting
AIS etc
End to end path trace
Offers WAN type framing (SDH/SONET) with Ethernet characteristics that modern engineers are familiar with
End-to-end visibility not seen in LAN-PHY
LAN-PHY interface: monitoring relies on upper layer protocols

## Slide 5: Moving Forward
What is Happening?
  Increased use of 100G in NREN and core links
  DCI solutions not compatible with WAN-PHY
  400G interfaces around the corner
  WAN-PHY not supported beyond 10G (OC192/STM64 rates)
  Juniper MX204 does not support WAN-PHY interfaces

## Slide 6: What about Monitoring?
Why is WAN-PHY good for NMS ?
  End to end visibility
  SNMP traps based solutions such as GEANT uses
GEANT RTR
NTU
CUSTOMER
X
OK
End to End Data flow Broken
GEANT NMS

## Slide 7: Mitigation?
ICMP monitor – Not currently part of GEANT core NMS
Upper protocol monitoring – Partly integrated into GEANT NMS where appropriate
LAG (LACP) minimum links
BFD…Bidirectional Forwarding Detection

## Slide 8: How is GEANT managing DCI links in the core
Minimum links = 3
One failure results in LACP channel showing DOWN – SNMP Trap generated
Adequate bandwidth in core to cope, G30 very reliable
DCI
DCI
GNT Router
GNT Router
OPTICAL
TXPNDR
OPTICAL TXPNDR
3 x 100G
3 x 100G
Fibre

## Slide 9: GEANT Reference Topology 2020+
WARNING – Reference design is NOT finalised by NRENs

## Slide 10: BFD in GEANT
Evolution:
ISIS BFD
Family BFD (IPv4 and IPv6)
LACP based microBFD (where we are now) – RFC 7130
  Monitors each LAG component

## Slide 11: BFD in GEANT

## Slide 12: BFD in GEANT
NTE or not, LACP ensures end-to-end forwarding on the link at layer 2, with failure interval of ~3 sec. - This covers most failure scenarios. LACP has its own component detection (GEANT set at 1s), BUT…
uBFD sitting on top of this ensures end-to-end forwarding on the link at layer 4, with failure interval 300ms
  uBFD pulls down the link if LACP does not
GEANT is extensively configured for LACP even with single physical links
Backbone – uBFD standardised everywhere.

## Slide 13: NOTE – Firewalls – UDP port required
set firewall family inet filter ROUTER_access term uBFD_accept from source-prefix-list geant-address-space
set firewall family inet filter ROUTER_access term uBFD_accept from protocol udp
set firewall family inet filter ROUTER_access term uBFD_accept from port 6784
set firewall family inet filter ROUTER_access term uBFD_accept then accept
insert firewall family inet filter ROUTER_access term uBFD_accept after term BFD_accept

## Slide 14: BFD with NREN links
NOT currently standard
Some NRENs have requested it at BGP level

## Slide 15: BFD with NRENs
Always receiving BGP down traps
  But maybe not always Interface traps
Most NREN links are direct patch connections meaning there is no problem as there would be no link carrier
BGP BFD is not the answer where multiple LAG components exist
Non BGP links with GEANT where NTUs exist – greatest risk here
GEANT may use BFD with NRENs under some circumstances to support link monitoring
  Discuss ?
  ICMP based reachability augmentation ?
  What about interoperability issues ?
Likely better at BGP protocol level

## Slide 16: OAM/CFM
In place in GEANT backbone
  Little used by engineers though as other tools suffice
But, due to deployment capabilities this is unlikely to happen

## Slide 17
Click to edit Master title style
Click to edit Master text styles
  Second level
    Third level
      Fourth level
        Fifth level
18/06/2020
17
Thank you
www.geant.org
Any questions?
© GÉANT Association on behalf of the GN4 Phase 2 project (GN4-2).
The research leading to these results has received funding from
the European Union’s Horizon 2020 research and innovation programme under Grant Agreement No. 731122 (GN4-2).