## Slide 1: Wi-Fi Network Monitoring with GÉANT WiFiMon
18-OCT-2023
Nikos Kostopoulos (NTUA/GRNET, Greece)
Elisantila Gaci (RASH, Albania)

## Slide 2: Introduction

## Slide 3: WiFiMon GÉANT Service
Monitoring Wi-Fi performance as experienced by end users
Combination of crowdsourced & hardware probe measurements
IEEE 802.1X networks (eduroam): Data from RADIUS & DHCP logs for richer analysis, e.g. per Access Point (AP)
Contribution:
Detection of Wi-Fi throughput degradation
Determination of underperforming areas within a Wi-Fi network
 Admins may enhance performance, e.g. by installing more APs

## Slide 4: WiFiMon vs Related Monitoring Tools
Monitoring from the end-user perspective (end-user experience)
No requirements for app installation or end-user intervention
Centralized view of Wi-Fi performance available to the administrator

## Slide 5: Example: WiFiMon vs Ookla Speedtest
WiFiMon | Ookla Speedtest
Automatically by visiting a site | By pressing “GO”
Wi-Fi administrator | End users
Measurements are triggered:
Results collected by:

## Slide 6
WiFiMon Operation
WiFiMon Components:
WiFiMon Software Probes (WSPs)
WiFiMon Hardware Probes (WHPs)
WiFiMon Analysis Server (WAS)
WiFiMon Test Server (WTS)

## Slide 7: Components

## Slide 8: WiFiMon Test Server (WTS)
Purpose: Holds code and test data for performance measurements
Based on JavaScript (JS) technology
HTML script tags pointing to test tools added to frequently visited sites
WTS Placement: Close to the monitored networks
(RTT between end devices and WTS included in results)
 If impossible: WiFiMon captures relative performance changes
2 available test tools:
Akamai Boomerang
LibreSpeed Speedtest

## Slide 9: WiFiMon Software Probes (WSPs)
End-user devices
Crowdsourced measurements triggered against the WTS when users visit a WiFiMon-enabled site
No requirement for additional software within user devices
Repetitive measurements regulated via a cookie value

## Slide 10: WiFiMon Hardware Probes (WHPs)
Wi-Fi performance measurements from fixed points within the network
Baseline throughput that complements crowdsourced measurements
Performance measurements similar to WSP ones
Additional data about monitored and nearby ESSIDs
TWAMP Measurements, System data (CPU, memory, etc)
Triggering measurements based on crontabs
Tested for Raspberry Pi v3 and v4

## Slide 11: WiFiMon User Interface (1)
Results per WHP
Aggregated Results

## Slide 12: WiFiMon User Interface (2)
Dashboards available for:
Average values
Median values
Maximum values
Minimum values
95th Percentile values
Sources:
Crowdsourced measurements
Hardware Probe measurements
Depicting estimations of:
Download throughput
Upload throughput
HTTP ping Round Trip Time (RTT)
That may be:
Uncorrelated
Correlated with the available APs

## Slide 13: Correlation with RADIUS/DHCP Logs
Correlation options:
With end-user IP address (only RADIUS logs)
With end-user MAC address (both RADIUS & DHCP logs)
Personally Identifiable Information: IP/MAC addresses secured in transit using TLS-encrypted channels and stored hashed in WAS (X-Pack)
Logs are:
Extracted from RADIUS/DHCP servers using Filebeat
Processed and transformed by Logstash in WAS
Stored in Elasticsearch of WAS

## Slide 14: Installation

## Slide 15: Installation Options
Institutions install all components on their premises
- Ansible playbook for WAS/WTS automated installation
- All data stay within the institution premises
Manual WAS installation: Abandoned by WiFiMon
NMaaS (simpler option for testing/trying WiFiMon)
- Another GÉANT Service
- WiFiMon WAS instance deployed on NMaaS
- WTS installation still required by institutions
(should be close to the monitored network)
NMaaS Portfolio

## Slide 16: WiFiMon Evolution

## Slide 17
WiFiMon Evolution
17
WiFiMon is born
2015
First presentation at
TNC15, Porto
2015
WiFiMon pilots in TNC19 and GÉANT Symposium 2020
2019-2020
WiFiMon declared official GÉANT service
2020
Cloudifying WiFiMon
2020
Automating server components
2021
Eduroam support
Additional Data Sources
2022
Probe control made easy
2023

## Slide 18
WHP Configuration & Control
Old approach
Administrator feedback demonstrated limitations:
In NAT networks
In public networks
Administrators edit config directly
Novel approach required!!!
Remote & user-friendly configuration of WHPs from a central point (WAS)
Flexibility to control WHPs behind NAT networks

## Slide 19
Configuration Made easy
Administrators (re)configure WHPs from the WiFiMon UI
Configuration files are generated based on Jinja2 templates
Provided data:
Device ID
FQDNs/IP addresses of WiFiMon components
Location information

## Slide 20: Remote Configuration Made Possible
Based on Salt
WAS Salt Master
WHPs Salt Minions
Configuration files generated from templates transferred from the WAS to WHPs
1
2
Salt includes a ZeroMQ message broker: Parallel configuration regardless of the WHP number
3
Salt establishes application layer communication: - WHPs remotely configured from the WAS
Reconfiguration easier for WHPs behind NAT
Public IP addresses not required
 IP space is conserved

## Slide 21: Thank you
18-OCT-2023
Homepage: https://wiki.geant.org/display/WIF
WiFiMon mailing list: wifimon-ops@lists.geant.org