## Slide 2: WiFiMon: Introduction
Monitoring Wi-Fi network performance as experienced by end users
Purpose:
Detection of Wi-Fi throughput degradation
Determination of underperforming areas within a Wi-Fi network
 Admins may enhance performance, e.g. by installing more APs
Main sources of data:
End users roaming the network  WiFiMon Software Probes (WSP’s)
Fixed-point devices  WiFiMon Hardware Probes (WHP’s)
WHP’s enable baseline comparisons for WSP measurements
WiFiMon Analysis Server (WAS): Centralised processing and control

## Slide 3: WHP Configuration & Control
WHP’s are installed by various NREN’s and Universities
Feedback from Administrators demonstrated limitations for setups with several WHP’s:
In NAT networks, reconfigurations require physically connecting to WHP’s
In public networks, remote SSH connectons require static IP’s  reduced flexibility
Administrators must edit configuration files themselves (hard, error-prone)
Novel approach required!!!
Remote & user-friendly configuration of WHP’s from a central point (WAS)
Ability to control WHP’s behind NAT networks

## Slide 4: WHP Configuration Made easy
New feature integrated within the WIFiMon User Interface (UI)
WiFiMon Administrators (re)configure WHP’s from the WiFiMon UI instead of manually editing configuration files
Configuration files are generated based on Jinja2 templates
Provided data:
Device identification number
FQDN’s/IP addresses of WiFiMon components
Location information

## Slide 5: Remote WHP Configuration Made Possible
Solution based on the Salt infrastructure management tool
WiFiMon Analysis Server  Salt Master
WiFiMon Hardware Probes  Salt Minions
Configuration files generated from templates are pushed from the WAS to the respective probes
1
2
Salt includes a ZeroMQ message broker: Parallel configuration regardless of the WHP total number
3
Salt establishes application layer communication: - WHP’s are remotely configured from the WAS
Remote reconfiguration possible even for WHP’s behind NAT
Static IP addresses are not required  Flexibility
Why not Ansible???  Agentless, but requires SSH