## Slide 2: Introduction

## Slide 3: WiFiMon: Introduction
Monitoring Wi-Fi network performance as experienced by end users
Combination of crowdsourced and hardware probe measurements
IEEE 802.1X networks (eduroam): Data from RADIUS and DHCP logs strengthen analysis options, e.g. per Access Point (AP)
Contribution:
Detection of Wi-Fi throughput degradation
Determination of underperforming areas within a Wi-Fi network
 Admins may enhance performance, e.g. by installing more APs
WiFiMon vs other monitoring solutions:
Monitoring from the end user perspective (end user experience)
No requirements for end user intervention or installation of apps
Centralized view of Wi-Fi performance available to the Wi-Fi administrator

## Slide 4: Example: WiFiMon vs Ookla Speedtest
WiFiMon | Ookla Speedtest
automatically by visiting a site | by pressing “GO”
the Wi-Fi administrator | the end users
Measurements are triggered:
Results are collected by:

## Slide 5: Design Features & Operation

## Slide 6: Design Features of WiFiMon
Combination of crowdsourced and hardware probe measurements
Correlation with RADIUS and DHCP logs respecting end user privacy
Independence of Wi-Fi technology and hardware vendor
Lightweight, active monitoring without significant impact on end user browsing experience

## Slide 7: Components
WiFiMon Software Probes (WSP’s): Wi-Fi enabled end user devices, e.g. laptops and smartphones, that trigger crowdsourced measurements
WiFiMon Hardware Probes (WHP’s): Devices that trigger measurements from fixed locations within the Wi-Fi network to complement crowdsourced measurements (e.g. Raspberry Pi’s)
WiFiMon Test Server (WTS): Holds code and test data required for WSP/WHP performance measurements
WiFiMon Analysis Server (WAS): Central processing component of WiFiMon that collects, processes, correlates and stores measurements as well as provides visualizations to WiFiMon administrators

## Slide 8: Reported Measurements
Performance Measurements: Estimations of download/upload throughput and HTTP Ping Round-Trip Time (both crowdsourced and hardware probes measurements)
Wireless network metrics: Bit rate, link quality, signal level and TX power from the WLAN NIC (hardware probes) – information about monitored and nearby ESSID’s
System metrics: CPU, memory and storage statistics (hardware probes)
Two-Way Active Measurement Protocol (TWAMP) measurements: Bandwidth, latency and packet loss estimations from TWAMP measurements among hardware probes and the WTS (hardware probes)

## Slide 9: WiFiMon Operation
WiFiMon Components:
WiFiMon Software Probes (WSPs)
WiFiMon Hardware Probes (WHPs)
WiFiMon Test Server (WTS)
WiFiMon Analysis Server (WAS)

## Slide 10: Installation

## Slide 11: WiFiMon Installation
Institutions install all components within their premises
- Ansible playbook for WAS automated installation
- Manual installation for WTS
- All data stay within the institution premises
- Support from WiFiMon team for all components
Manual WAS installation: Abandoned by WiFiMon
NMaaS (more appropriate for testing/trying WiFiMon)
- Another GÉANT Service
- WiFiMon WAS instance deployed on NMaaS
- WTS installation still required by institutions
(should be close to the monitored network)
- Support from WiFiMon team for interfacing
WTS and Dockerized WAS on NMaaS
NMaaS Portfolio
Options:
GÉANT Service since 2020!

## Slide 12: WAS NMaaS Installation (1)
Login to NMaaS platform via Federated Login

## Slide 13: WAS NMaaS Installation (2)
Selection of WiFiMon from the NMaaS Portfolio of services

## Slide 14: WAS NMaaS Installation (3)
Name the new instance
Select the version of the new instance
Deploy the instance

## Slide 15: WAS NMaaS Installation (4)
Define the specifications of the new instance
Wait for the deployment of the instance

## Slide 16: Ansible WAS Installation
Specs (minimum/recommended):
4 CPU cores
8 GB / 16 GB RAM
10 GB / 50 GB Free Space
Operating Systems Tested:
Debian 10
Debian 11
Ubuntu 18.04
Ubuntu 20.04
Other Requirements:
Ansible (and its requirements)
Root access
Appropriate DNS records
Filling details (e.g. passwords)
within a file (see figure)

## Slide 17: WiFiMon User Interface

## Slide 18: WiFiMon User Interface (1)
Login to WiFiMon UI using UI credentials

## Slide 19: WiFiMon User Interface (2)
Measurement results are protected by X-Pack ELK plugin
X-Pack credentials are also required

## Slide 20: WiFiMon User Interface (3)
Define the Wi-Fi subnets to monitor
Excludes end users visiting WiFiMon websites from wired segments or other Wi-Fi networks

## Slide 21: WiFiMon User Interface (4)
Overview tab: Overview of daily measurements

## Slide 22: WiFiMon User Interface (5)
HW Probes tab: Download throughput estimations using multiple probes and the available test tools (NetTest, Akamai Boomerang, LibreSpeed Speedtest)

## Slide 23: WiFiMon User Interface (6)
HW Probes tab: Upload throughput estimations using multiple probes

## Slide 24: WiFiMon User Interface (7)
HW Probes tab: HTTP Ping Round Trip Time estimations using multiple probes

## Slide 25: WiFiMon User Interface (8)
HW Probes tab: Metrics from probes (Bit rate, Link quality, Signal level, TX power)

## Slide 26: WiFiMon User Interface (8)
Ability to report average/median/minimum/maximum/95th percentile values

## Slide 27: WiFiMon User Interface (9)
Support for TWAMP measurements among probes and WTS

## Slide 28: Additional Features, Future Steps and Useful Links

## Slide 29: Other Features of WiFiMon
Notification of WiFiMon version updates
- WiFiMon Users are informed of new versions from the UI
- Enables monitoring WiFiMon utilization (optional feature)
Log Exporter specifically designed for eduroam
- WHP data exported towards the JSON collector of eduroam (optional)
- May be used with any JSON collector
WTS location information
- Facilitates using multiple WTS instances
- Monitoring multiple sites with a single WAS
IPv6 Support
End User Number Approximation (currently tested)
Ping Statistics

## Slide 30: Future Steps
Enrichment of monitoring tools
Automatic prediction of Wi-Fi performance drops (Time series analysis)
Automatic correlation between crowdsourced and probe measurements
Monitoring campus environments

## Slide 31: Check out the WiFiMon video!
https://www.youtube.com/watch?v=9LuGlF6JSnA
… or the WiFiMon Infoshare
https://www.youtube.com/watch?v=VXQV2zWRKgo
https://wiki.geant.org/display/WIF/WiFiMon+Publications
… or previous presentations
… or the WiFiMon paper at IEEE/IFIP WONS 2021
http://dl.ifip.org/db/conf/wons/wons2021/1570695031.pdf