## Slide 1
Stefan Winter
JRA3 Kick-Off Meeting, Zürich
eduroam development - plan
JRA3-T4
12 July 2016
Task Leader JRA3-T4
R&D Engineer, RESTENA Foundation

## Slide 2: Work Areas
eduroam-as-a-service, comprising
  IdP-as-a-service (“Silver Bullet IdP”)
  SP-as-a-service (“No fancy name”)
Self-Service Support
  for end users (“Why am I not online?”)
  For admins (“I need to talk to IdP/SP X because…”)
CAT “business as usual” development
  new devices like Kindle
  beefing-up of current installers (more Passpoint support...)
Let’s RadSec

## Slide 3: IdP-as-a-service
“Silver Bullet” IdP
  EAP-TLS based
  “IdP” admin gets simple web interface to manage own users
Requires
  CA which issues/revokes user certificates in real-time
  RADIUS server(s) which terminate EAP-TLS and do actual authentication
    More than one? Decentralisation difficult due to EAP server verification!
  Management UI for the admins
Exploits
  Availability of installer generation engine in eduroam CAT (“just yet another EAP type”)
  Existing admin UI in CAT for the config parts unrelated to Silver Bullet
    Additional SSIDs
    Institution Logo
    Helpdesk contact details
    … you name it

## Slide 4: SP-as-a-service
Just an ordinary proxy-only RADIUS server
Best-of-class: implement all optional/recommended features we like to but seldomly do see in real life
Easy to distribute: central, NRO level, at the spot
With Let’s RadSec: uplink with eduroam SP certificate

## Slide 5: Self-Service
For users:
  integrate monitoring subsystems and real-time diagnostics into a cohesive and simple user experience
  give simple explanations / instructions / steps forward
  automate wherever possible
    e.g. instead of generic “contact your IdP”: show web form which will be sent to relevant contact at IdP – users do not need to know contact details themselves
    fallbacks in place (no IdP email known? Display phone, or send to NRO instead)
  Needs improvements in eduroam monitoring -> operations
For admins:
  automate workflows for common issues where flow was previously “contact your NRO and wait for guidance”
  typical use cases: abuse complaints, reject due to missing MAC address in request, informing SP of lack of IP addresses in DHCP pool, malformed Operator-Name
  web forms all around

## Slide 6: eduroam CAT
eduroam CAT
  Devices
    Not many “actually new” devices on the radar.
    Contrary, Windows Phone is dead!
    Kindle (FireOS) is mostly Android, but different enough to potentially be(come) difficult
  Features
    Passpoint now configurable on all our supported platforms (currently implemented only on iOS / OS X  room for improvement)
    Shift from install-once to a permanent assistance application on all platforms
      Initial installation
      Ongoing account management (check expiry and consequences, renew cert)
      Running diagnosis where needed
      Maps of coverage
      I would call it the “Companion” if that name weren’t already taken ;-)

## Slide 7: Let’s RadSec
RADIUS/TLS for server infrastructure is all nice
  But getting certificates too cumbersome in practice
  Need a more automated solution
Prototype can provision RADIUS/TLS server certificates to EAP servers fully automated
  EAP server == eduroam IdP
  security profile still under discussion
  Unfortunately, eduroam IdPs unlikely first adopters
  Rather expect trickle-down from NRO level
So, need a provisioning method for the other slice of servers
  NRO RADIUS proxies in top priority
  (then eduroam IdPs, mostly solved)
  eduroam SPs
CSR copy&paste to web form the likely best candidate for SPs and NRO