## Slide 1: Data Center Interconnection (DCI) over Spectrum Sharing CNAF-CERN
Paolo Bolletta
09/04/2024
14th SIG-NGN – Catania

## Slide 2: Outline
Spectrum Sharing
DCI interconnection and L3 Overlay
Data Challenge

## Slide 3: GEANT project and the Spectrum Connection Service (SCS) team
GÉANT network has been upgraded during last years.
A new Spectrum Connection Service (SCS) has been proposed in the GÉANT Network Evolution Plan
Activity started in GN4-3 WP7-T2 (SCS) and taken over in GN5-1 (NDS)
The SCS team
  has defined a service description
  is running field trials
  engages Users to run service pilots
Real Use Case CNAF-CERN:

## Slide 4: CERN – CNAF Data Centre Interconnection
Add/Drop
GEANT Open Line System
ROADM
8x AMP
Milan PoP
Geneva CERN DC
Add/Drop
GARR Open Line System
ROADM
3x AMP
Bologna CNAF DC
TRX
TRX
~ 1000 km
1.6 Tbps
        4 carriers
        DP-16QAM
        27% SD-FEC
        69 Gbaud
        75 GHz

## Slide 5: Quality of Transmission (Q-factor)

## Slide 6: Enabling Technology
Disaggregated optical network:
Open Optical Line System (~10y life span)
Coherent optical interfaces (~3y life span)
  Transponders boxes
  Pluggable transceivers

## Slide 7: DCI LHCOPN [CNAF-CERN] L3 vs. L1
Before - L3
RTT: 15ms
After – L1
RTT: 9.5ms

## Slide 8: Overlay: full picture

## Slide 9: Overlay: full picture
as-path 2038 - 513
as-path 2038 - 137 - 513
Public ASN required for BGP direct peering between CERN and CNAF

## Slide 10: LHCOPN – complete picture
Credits: CERN-WLCG wiki

## Slide 11: Data Challenge WLCG – [12-24/02/24]
From 12/02/24 to 24/02/24
Opportunity to verify if the network is ready and able to match WLCG needs and expectations
GREAT Opportunity to understand if a pure multidomain optical connection ( based on SCS) may be fully considered a stable and valid element in the WLCG networking
CNAF and GARR sprint aimed to include the new SCS connection as primary link for LHCOPN between CNAF and CERN (T0 -->T1)
Decision to use SCS connection for DC24 early December 2023
By mid-January setup implemented, tested and fully operational
Image credits: AI MS-Copilot

## Slide 12: OPN DCI Spectrum Sharing – CNAF CERN Data Challenge
OPN DCI Max IN: 136Gbps Max OUT: 289Gbps

## Slide 13: CNAF LHCONE VPN (L3)
LHCONE Max IN: 143Gbps Max OUT: 114Gbps

## Slide 14: CNAF LHC physical interface

## Slide 15: Failover
Fiber Cut

## Slide 16: Failover
Fiber Cut

## Slide 17: Next Steps
Pilot
400GEth interface evaluation
Satellite Sites integration --> new site BO06@Tecnopolo
Network to Network interconnection (@MI01) standardization process with GEANT
3rd party Planning Tool (GNpy)
Production
Channel diversification in order to improve interconnection resiliency
GEANT Geneva ROADM setup reshuffling
Transition from Pilot to Production Service (ongoing)
  4 x 100GHz channels:

## Slide 18: Conclusions
Solution ready to production and to scale-up and evolve
Network service model could be exported and adopted in other communities.
Pilot and development activities will continue
Alternative Cross Board Path should be investigated ?
Acknowledgments:
GARR Optical : Colantonio, Vuagnin
GARR Packet : Inzerilli, Marletta, Valiante
GARR DC & DevOps : Cesaroni, Chiarelli, Marzulli
CNAF Team: Zani, De Girolamo
CERN Team: Martelli
GEANT Team: SCS Team, Roberts
GARR Management/Amm/CTS
Contact:
paolo.bolletta@garr.it
infra.optical@garr.it
'image: Flaticon.com