## Slide 1: GÉANT Operations automation on perfSONAR
Ivan Garnizov ・ GÉANT / NOC pS systems engineer & perfSONAR Development Team ivan.garnizov@fau.de

## Slide 2: GÉANT Operations OC team
GN OC team, led by Tony Barber
  Network management and incidents
    Support perfSONAR
  Security incidents
  First line support team
Single point of contact: (support@oc.geant.net)

## Slide 3: GN Backbone and pS deployment PoPs
GÉANT backbone
R&E available servers
LHC VRF available servers

## Slide 4: pS server hardware deployment
Servers are 10Gb/s capable
Interfaces
  Physical
  VLAN
Assignments
  Management: psmp-gn-mgmt-par-fr.geant.org
  Latency: psmp-gn-owd-par-fr.geant.org
  Throughput: psmp-gn-bw-par-fr.geant.org

## Slide 5: perfSONAR configuration management
Puppet based automation
  cooperation between OC, DevOps, IT, Network Implementations
  modules based collaboration with Git backend
  applies T/U/P model for code
  management separation and sharing with DevOps
  Overlappings
  Template management in 2 stage
  Inheritance and overruling

## Slide 6: Main areas
Software versioning
OS specific customizations
Firewall
pScheduler
pSconfig
Lookup service

## Slide 7: Software versioning
Repository snapshots
Deployment version control for rebuilds and new servers
perf_role::perfsonar::psrepo: '5.0.8'
'perfsonar_focal': os_release => '20.04', repo_name => 'perfsonar', snapshot_purge => ['04.09.2023'], snapshot_names => ['5.0.6', '5.0.8'], deb_line => 'deb http://downloads.perfsonar.net/debian perfsonar-release main';

## Slide 8: OS specific customization
VLAN, IP, Hostname
Source routing
Disk partitioning LVM
System optimizations
  Network card
  TCP stack

## Slide 9: FW configuration
Based on service descriptions
Interface assignments to service descriptions
Strict FW Ingress and Egress management
  Egress (source port & destination port)
Issue
  pScheduler schedule

## Slide 10: pScheduler Limits
Limits configuration
  Identifier (which other)
  Limits
    automatic rules for generic interface assignments
  Applications
  Priorities

## Slide 11: pSconfig management
Management of multiple pS mesh sources
  Inheritance
  (De)activation of measurement archive
Default measurement archive
  pScheduler task param
  Inheritance
  (De)activation of measurement archive

## Slide 12: Lookup service configuration
All fields managed
Specific interface registrations:
  http://35.223.142.206:8090/lookup/host/4211b758-2671-4dae-a7f9-5b4e61bfd265

## Slide 13: Questions? ivan.garnizov@fau.de