## Slide 1: Network Function Verification using Open Source Solutions
3rd SIG-PMV @ NORDUnet, Copenhagen, 2017-11-28
Notes: Thanks for having me
Presenting past ~year of research, which sets the scene for future work
Gathering the tools, researching the problems, exploring how to test them

## Slide 2: What: Open Source Network Function Validation
Open source, synthetic, in-band, network function validation and performance testing:
Open Source: Specifically OSS runs on Linux (happy to pay but not to compromise on scale/features/security/standards compliance)
Synthetic: This means the ability to simulate production traffic (or replay it) to provide reliable A/B testing
In-Band: Focus on the data plane level (many operators are solving ctrl/mgmt plane using CI/CD processes)
Notes: Bit of a mouth full!
We want to experience the network exactly as the end user/application does
In-band, within the same LSP for example

## Slide 3: What: Open Source Network Function Validation
Network Functions: Not all traffic passes through the same set of network functions when using NFV or SR:
  Load-balancing e.g. (un)-ECMP/LAG/Geo/Session
  Fast-reconvergence e.g. IP FRR (r)LFA/MPLS-TE FRR/BGP PIC
  Traffic filtering e.g. BUM filters (Ethernet)/uRPF (IP & MPLS)
Notes: NFs create abstracted/strictly defined versions of these well known functions
RFC4364 - BGP/MPLS IP Virtual Private Networks (VPNs)
IOS + “mpls ip”

## Slide 4: Why: Fail-safe and assume it doesn’t work
http://www.testequipmentdepot.com/viavi/images/csc-ethernet.jpg
Was the exact same frame received that was sent?
Traffic flow
Schrodinger’s Router
Secret routing magic happens here
Frame Tx
Traffic flow
Frame Rx
?
Notes: No reference to JDSU, just a generic tester image!
Open source is key
Traffic types: PPPoE being supported over L2VPN was undocumented
Test types: RFC2544 (1999) isn’t a strict definition, ITU-T Y.1564 is “better”

## Slide 5: Why: Fail-safe and assume it doesn’t work
Testing in general:
“If you haven’t tested it, it doesn’t work!”
Black box vendor devices with undocumented behaviour
Troubleshooting might require TAC assistance and/or hidden commands
Currently black box vendor devices being tested with black box testers
“We can’t test every possibility in the lab”
Notes: Open source is key
Cisco undocumented behaviour caused an outage
Juniper denied me access to packet-via-dmem and ttrace / IOS-XE Bash shell required TAC authentication token
Vendors aren’t bad, happy to pay for support but I don’t want to depend on it

## Slide 6: Where: Ideally in the lab
Mainly testing physical devices in the lab (sometimes in production)
However, we’re exacerbating the issue with the rise of NFV and COTS (SD-WAN, vCPE, vPE, vRR, vBNG)
We’re running black box virtual network functions!
  Obvious issue: COTS is by definition not task optimised
  Less obvious issue: how many additional variables COTS introduces
NFV is an interesting area for open source (OVS+DPDK, VPP)
Caveat: white box hardware is not open source hardware
Notes: One vendor provides us an “all-in-one” image for COTS
Intel Management Engine security issues

## Slide 7: Where: Physical network devices
Historically only expensive hardware testers could test high bandwidth links
Initially testing layers 2/2.5 (Ethernet/MPLS) and moving into layer 2/2.5 VNFs
Both lack security, MPLS is for transport and has no encapsulation support:
  E.g. does it even work? Hashing on Broken Assumptions
  E.g. ECMP with L2 and L3 VPNs is inherently flawed due to a heuristic methodology. Old problem BCP128 (2007), still an issue draft-ietf-pals-ethernet-cw-00.txt (2017!)
Notes: Multiple iPerf flows with different DSCP values for QoS testing isn’t new

## Slide 8: Where: Virtualisation paths
Hypervisor
Virtual Router
(secret routing magic)
Virtio B/E
Virtio F/E
Host OS
NIC
Bridge
TAP
Virtio F/E
Virtio B/E
NIC
Bridge
TAP
Hypervisor
Virtual Router
(secret routing magic)
vNIC
Host OS
PF
VF
vNIC
PF
VF
Traditional vs. modern VNF network path on Linux:
Notes: In the case of Service Chaining the “chain” varies by user/flow

## Slide 9: When: Ad-hoc not continuous
Staging and soak testing phases for individual network functions
A localised approach, device-by-device, feature-by-feature
Support automated benchmarking and CI/CD processes with data-plan testing in virtual-labs
Notes: Draft In-situ OAM provides continuous in-band monitoring with packet headers

## Slide 10: How: Linux & OSS PMV Tooling
Passive, synthetic, in-band traffic generation (or replay)
A localised approach, device-by-device, feature-by-feature
Traffic volume (bandwidth) is rarely an issue the focus is more on functionality, but still in scope to fully move away from black box hardware testers
Prefer open source to maximise on features/distribution/support/bug fixes etc.

## Slide 11: How: Linux & OSS PMV Tooling
https://commons.wikimedia.org/wiki/File:Osi-model-jb.svg
MoonGen, Pktgen
Pktgen, MoonGen, Etherate
iPerf, Trex, Scapy
CRC/FCS, ECC

## Slide 12: How: Linux & OSS PMV
No transport layer testing:
Including the end-user/end-device networking stack is like Russian roulette
i.e. TCP OS implementations are too varied and too complicated
iPerf3 in UDP mode, only of if you have to
Recent Improvements in UDP Packet Processing: UDP throughput went from 1.2 Mpps in Kernel 4.9 to ~2.25 Mpps in Kernel 4.13
Two raw socket applications on Linux aren’t even the same
Notes: 4.9 > 4.13 is circa one year
RX timestamping can be configured per-socket in Linux

## Slide 13: How: Linux & OSS PMV
Etherate: Raw socket based Ethernet and MPLS packet generator
  Any layer 2/2.5 header value (load packet-as-hex fall back)
  Constraint based testing (time/speed/volume)
  Easy CLI usage (no API / not scriptable)
  Hardware agnostic
  Lowest performance
  Stateless
https://commons.wikimedia.org/wiki/File:Green_tick_pointed.svg
https://commons.wikimedia.org/wiki/File:Red_X.svg
Notes: It’s fun to give your self a green tick
EtherateMT is in the pipeline for higher throughput and testing different Linux syscalls

## Slide 14: How: Linux & OSS PMV
Pktgen: DPDK based packet generator using LuaJIT
  Most layer 2-4 header options (load PCAP as fall back)
  “Range” and “sequence” native features
  All options in CLI and Lua API (scriptable)
  Highest performance
  Requires DPDK supported NIC
  Stateless
Notes: Not the Kernel module of the same name!
Supports Ethernet/QinQ/MPLS/IPv4/TCP/UDP/ICMP/GRE
Higher performance then MoonGen on my Intel X710
Only “rate” constraint exists natively

## Slide 15: How: Linux & OSS PMV
MoonGen: DPDK based packet generator using LuaJIT
  Any layer 2-4 header options
  No CLI options, scripted tests only (Lua API)
  Partially stateful
  High(er) performance
  Requires DPDK support NIC
  DPDK EAL settings are hidden
Notes: No MPLS support
Supports Ethernet/ARP/IPv4/IPv6/TCP/UDP/ICMP/ESP/AH/PTP
Can’t see NICs before test starts or configure CPU mask etc.

## Slide 16: How: Tooling Comparisons
Etherate assumes two difference devices are being used. MoonGen & Pktgen assume the Tx and Rx hosts are the same device.
Etherate can be used to test a physical device or link at layers 2/2.5. Pktgen & MoonGen can be used to test a physical device or link at layers 2-4 for high performing metrics (high throughput or low latency)
Etherate can also test the raw socket path within the Kernel networking stack. PktGgen & MoonGen can also provide some low level NIC stats.

## Slide 17: Examples: NF Verification using OSS
Example resources/guides:
Evolving document: Linux and NFV Testing and Tuning
Example MoonGen Lua script: generate every Ethertype (0x0000-0xFFFF)
“We can test every possibility in the lab”

## Slide 18: Examples: BUM filter accuracy
NIC: Intel I350 1G, DUT: Cisco 2960, Test: Etherate broadcast test 2960#show storm-control fa0/15
Interface Filter State Upper Lower Current
--------- ------------- ----------- ----------- ----------
Fa0/15 Forwarding 0.25% 0.25% 0.24%
$ sudo ./etherate -i eno2 -g -G -d FF:FF:FF:FF:FF:FF -M 250000
Seconds Mbps Tx MBs Tx FrmTx/s Frames Tx
1 0.24 0 20 20
2 0.24 0 20 40
Notes: Etherate frame pacing feature should provide different results?

## Slide 19: Examples: Every Ethertype value
NIC: Intel I350 1G, DUT: Cisco 2960, Test: MoonGen “setType” ethertype
Rx NIC drops ~1400 frames, from etype 0x2F to 0x5DC, 0x8100, and 0x888e
Random missing Ethertype chosen and retested, 0x2F == 100% lost
Random working Ethertype chosen and retested, 0x2E == 100% received
0x2E-0x5DC are length values for 802.3 Ethernet + LLC/SNAP (802.2) framing
0x8100 (802.1q VLAN tag): 0 packets input, 65536 runts
0x888e (802.1X EAP): 65536 packets input, 0 errors/drops/runs/discards
“switchport mode access” / No 802.1X configured
Notes: Ethertypes are supposed to start from 0x600 (1536)

## Slide 20: Examples: Every Ethertype value
NIC: Intel X710 10G, DUT: ASR9001, Test: MoonGen “setType” ethertype
Rx NIC drops ~8500 Ethertypes
0x8808 (802.3x “pause”) 0 packets input, no NP counters
0x88a8 (802.1ad QinQ/PB), 0x9100 and 0x9200 (802.1q QinQ):
NP Counter: PARSE_DROP_IN_UIDB_TCAM_MISS
Notes: ASR9000s support multiple VLAN etypes; 8100, 88A8, 9100, 9200

## Slide 21: Examples: Every Ethertype value
NIC: Intel X710 10G, DUT: ASR9001, Test: Pktgen performance/size distribution
Pktgen:/> set 0 size 247
Pktgen:/> start 0
NP Counters:
PARSE_TOP_LOOP_RECEIVE_CNT 5987587286 6742449
MDF_PIPE_LPBK 5987589832 6742451
MDF_PIPE_LPBK_BUFFER_PREFETCH 2963853909 3371225
Notes: CSCvf44769 specifies a 33% throughput reduction
Easily detectable using RFC2544

## Slide 22: Example: In-flight bit errors
https://commons.wikimedia.org/wiki/File:Router.svg
CPE1
PE1
PE2
CPE2
Ethernet
IP
TCP
DATA
CRC
Checksum
Checksum
Ethernet
MPLS
Ethernet
IP
TCP
DATA
CRC
Checksum
Checksum
Ethernet
IP
TCP
DATA
CRC
Checksum
Checksum
MPLS is a transport protocol, not an encapsulation protocol:
Notes: Drawing in PP isn’t fun
CRC will only detects errors
CRC covers the entire frame but only over the link

## Slide 23: Example: In-flight bit errors
https://commons.wikimedia.org/wiki/File:Router.svg
CPE1
PE1
PE2
CPE2
Some vendors have NPU counters (which are exposed via SNMP):
  E.g. Cisco ASR9K: PARSE_DROP_IPV4_CHECKSUM_ERROR
  E.g. Juniper: bad-IPv4-hdr
No known tooling to test this end to end
Unprotected
Unprotected
Protected
Protected
Protected
Notes: ECC memory detect and often recover
Not all aspects of network devices use ECC memory

## Slide 24: Example: NFV and COTS
Host VNF Paths | VNF Considerations
NAT: slow and inflexible (L3/L4 only) | These techniques are mostly agnostic to the guest VM/application however the Linux native networking stack is slow(-ish)
Linux bridging: slow but flexible | 
PCI-PT: fast and flexible, but costly | 
SR-IOV: fast, flexible, cost efficient (not perfect yet, e.g. VLANs/Multicast) | Requires VM/application support
Kernel-Bypass (DPDK/Snabb/NetMap); fast, flexible, cost efficient | Proven technologies, limited commercial support adoption
XDP and/or rDMA; native support for Virtio on the horizon | Bleeding edge, immature for now
Notes: Mellanox eSwitch for SR-IOV
Snabb used on Deutsche Telekom’s TeraStream
DPDK used in VPP/vMX/ASR9Kv

## Slide 25: Example: NFV and COTS
Even with close source solutions we can peak into their performance:
  Open Process Counter Monitor – Intel focused CPU/NUMA/PCI/RAM/Power performance profiling
  Perf “perf_events” – Kernel and application performance using Kernel tracepoints and kropes/uprobes (and more!)
  SystemTap – Kernel and application performance profiling using Kernel tracepoints and function calls/returns (and more!)
Notes: Valgrind / cachegrind / callgrind are essential if you write your own tester
SystemTap regularly used for histograms

## Slide 26: Future: Recap of work until now
Research from the past ~year has been presented
  Researched the existing problems (currently using ADE 651!)
  Evaluated the existing open source toolset
  Defining tests to detect known issues
  Trying to fill some gaps in test features
Combine all of the above into an open guide for low level testing.
https://en.wikipedia.org/wiki/ADE_651#/media/File:ADE_651_at_QEDcon_2016_01.jpg
Notes: The ADE 651 is a fake bomb detector

## Slide 27: Future: Next steps / key takeaway points
Evolving document: Linux and NFV Testing and Tuning
Etherate; frame pacing, bit fiddling, frame checksums
EtherateMT; coming soon for faster kernel path testing
MoonGen & Pktgen: Fix RFC2544 test scripts and/or implement ITU-T Y.1564
Document SystemTap, perf and OPCM examples

## Slide 28: Future: Next steps (long term)
Better equipped and experienced to implement and profile NFV and COTS
Replace P nodes with VPP+FRR (or equivalent) on COTS for “quick win”
P4 FPGA for reliable open source hardware tester replacement?
Notes: Fully open source hardware and software testers

## Slide 29: Questions?
Contact me using these details:
Email: jwbensley@gmail.com / james.bensley@updata.net
Slack: http://networktocode.slack.com/
Skype: jameswbensley

## Slide 30: Extra: Background
James Bensley / Platform Architect / SP NetEng + Linux + coding
Updata Infrastructure (Capita Networking Services)
Originally formed in 2003, CNS-WAN has 500+ employees today
ISP and Managed WAN Provider
UK based LLU provider (CLEC)
Present in 1200 exchanges UK wide
Business, Local Gov, Edu, Health Care, Fire & Rescue, Police
Notes: ~12% UK Schools connected National Air Traffic Services (low bandwidth, low latency, very high resilience)
Health and Social Care Network (high bandwidth, filtered Internet)

## Slide 31: Extra: Easily testable bugs
Example bugs which could have been easily caught with better testing:
PPPoE unsupported over L2VPN (undocumented ASR920 core encapsulation)
Interop LDP PWE3 label request (IOS-XR CSCux80490)
LPTS denying OSPFv3 incorrectly (IOS-XR CSCui29635)
NPU cache misses causes 33% performance drop (IOS-XR CSCvf44769)

## Slide 32: Extra: Tooling Comparisons
Complexity
Granularity
Trex
MoonGen
Pktgen
Etherate

## Slide 33: Extra: SIG-PMV overlap with IETF
IETF: Benchmarking Methodology Working Group: “…the BMWG is limited to the characterization of implementations of various internetworking technologies using controlled stimuli in a laboratory environment. Said differently, the BMWG does not attempt to produce benchmarks for live, operational Networks…”
https://datatracker.ietf.org/wg/bmwg/about/
Notes: Recently expanded scope to include SDN and NFV

## Slide 34: Future: Expanding the scope
Linux already supports: IPv6 Segment Routing, VRFs, EVPN, MPLS, LDP
Linux native improvements:
XDP and eBPF is already being used to provide fast packet processing
SR-IOV switchdev could be used for routing?
~50-60ns IPv4 lookups (single core / DDR) barely supports 10Gbps
~450ns IPv6 lookups (single core / DDR)

## Slide 35: Extra: Outline
Who: My background
What: Initial research on open source network function testing
Why: If you haven’t tested it, it doesn’t work
When: Ad-hoc not continuous, soak testing/break-fix
Where: Production WANs and lab environments
How: Simulate network traffic using open source software
Examples: My findings and lessons learnt (so far)
Future work: Planned areas of testing and tooling development